## Slide 1: Electronics 101

## Slide 2: DISCLAIMER
At first, we will look at a very small subset of electrical engineering
Specifically, for the time being, we’re focusing on steady-state circuits
  That is, everything stays the same over time; there are no pulses, for example, or sine waves, or signals
A lot of the things that I will say are wrong in the general sense
  For example, “electricity can’t pass through an insulator”
Understand that these things are simplifications that make electronics easier to understand under specific circumstances, but are not always true
I’ll make it clear when I’m saying something that is a real, no-shit physical law (it’ll be in red)

## Slide 3: The “Water Analogy”
Often, I’ll compare electrical processes and components to flowing water, pipes, etc.
Again, these are approximations that are intended to help give an intuitive understanding of electricity, but that shouldn’t be taken too far

## Slide 4: Electrical Charge
Electrical charge is a measure of the “amount of electricity”
The SI unit of electrical charge is the coulomb
  Symbol: Q
Unlike mass (as far as we know), charge is not absolute; it can be positive or negative
This is not a transient or relative property; you can absolutely just cram some coulombs into an object
  This is basically what happens when you shuffle your feet on a carpet in dry weather
Water analogy: a Coulomb is a gallon of water

## Slide 5: Electrical Charge
“Opposite charges attract; like charges repel”
  Basic interpretation of Coulomb’s Law
  May or may not be true for dating
More specifically:
is “Coulomb’s constant”,

## Slide 6: Electrical Charge
This leads directly to the concept of the “electrometer”

## Slide 7: Current
Any charge (positive or negative) is conveyed by charge carriers
  Frequently, this implies electrons
  Electrons have negative charge
  Specifically, one electron carries -1.602 × 10-19 C
  Positive charge is often modeled as places that an electron wants to be, but isn’t
    These places are called holes
  E.g., if a BB has room for one more electron than it actually has, then it has one hole, or 1.602 × 10-19 C (positive charge)

## Slide 8: Current
The amount of charge passing a certain point in a certain amount of time
Measured in amperes (A)
  Usually abbreviated amps
  Symbol: I
1 ampere = 1 coulomb per second
Water analogy: fluid flow rate; gallons/second

## Slide 9: Current
Schematics often use constant-current sources
They force a constant amount of current to flow
1 A

## Slide 10: Voltage
How difficult it is to move some electrical charge from one point to another
Measured in Volts
  Symbol: V
Always a relative term
  I.e., voltage is between two points
  If not otherwise specified, voltage is assumed to be relative to the Earth (in electrical engineering) or an infinite distance away from a point charge (physics)
  Generally speaking, you can choose your reference (ground) to be anything you like, and the math will work out the same
  Ground or “Earth ground”:
  “Chassis ground”:

## Slide 11: Voltage
This is the symbol for a cell:
  Cells generate a constant voltage across their poles
This is the symbol for a battery:
  Batteries are made up of several cells
Usually, you just use a battery symbol, with the voltage written next to it:
Alternatively, a constant voltage source symbol may be used:
12 V
12 V

## Slide 12: Voltage
These circuits are identical, just with different choices of ground:

## Slide 13: Voltage
Water analogy:
  Pressure
  Similarly, pressure is usually assumed to be with respect to the atmosphere unless otherwise stated
  E.g., 10 PSI is pressure above atmosphere; -10 PSI is pressure below atmosphere (i.e. vacuum)
  Atmosphere is the “ground”
  However, you can also just measure the pressure between two pipes, without caring about the atmosphere

## Slide 14: Resistance
Resistance, as the name implies, resists or opposes the flow of current
Imagine a pipe with an orifice plate (a plate with a hole in it) in the middle
The same amount of water is flowing on both sides of the plate
However, the plate causes a pressure drop
The pressure drop is proportional to the flow rate
Higher pressure
Lower pressure

## Slide 15: Resistance
Resistors are discrete components that have a certain amount of resistance
They cause a voltage (pressure) drop that is proportional to the current (flow rate)
The proportionality constant is the resistance (R)
  E.g., how much voltage drop is generated per amount of current
  Measured in ohms
  Symbol: Ω
  The ohm is defined to be 1 V/A

## Slide 16: Resistance
That is, if you pass a current of 1 A through a 1 Ω resistor, it will create a voltage drop of 1 V
Likewise, if you apply a voltage of 1 V across a resistor, 1 A will flow through it
This is known as Ohm’s Law:
  Rearrange it algebraically as you like: ,
Resistor symbol:

## Slide 17: Kirchoff’s Laws
Two different laws fundamental to DC circuit analysis
First law: The sum of currents entering a junction must be zero
Second law: The sum of all voltage drops around a loop must be zero

## Slide 18: Kirchoff’s Laws
A loop is a continuous path through which current can flow
It does, in fact carry some current; the loop current
  (Although this can be zero)
Note that multiple loops can pass through a given wire or component
Loop with 1 A
Loop with 1 A
Therefore this component carries 2 A

## Slide 19: Kirchoff’s Laws
Simple circuit with one loop:
VR
(12)
+(-VR)
=0
VR=12
For a resistor:
+
-

## Slide 20: Kirchoff’s Laws
Slightly more complex example:
Goal: find and

## Slide 21: Kirchoff’s Laws
From Kirchoff’s 2nd law:
We have two unknowns () and two equations, so we should be able to solve:
E1:
E2:
Invert E2:
Combine:
Sub in actual values:
in the direction (or -0.128 in the direction)

## Slide 22: Kirchoff’s Laws
The specific loops you choose don’t matter!
Basically, as long as each component and wire has at least one loop passing through it, you can solve the circuit

## Slide 23: Kirchoff’s Laws
From Kirchoff’s 2nd law:
We have two unknowns () and two equations, so we should be able to solve:
E1: )
E2:
Combine:
Sub in actual values:

## Slide 24: Power
“Energy per time”
For example, water has a specific heat of ~1055 J lbm-1 °F-1
  In other words, you need 1055 joules of energy to heat up a pound of water by 1 degree Fahrenheit
Power is measured in watts (1 joule per second)
  Less commonly, horsepower or BTU per hour
If you have a heater that can put out 1 W, it will take you 1055 seconds to heat up a pound of water by 1 °F
Likewise, a 100 W heater will do it in ~10.5 seconds

## Slide 25: Power
In electrical terms, power is the product of voltage and current
Commonly formulated as
  Easily found by combining with Ohm’s Law

## Slide 26: Power
Power is a signed quantity; it can be positive or negative
By convention, things which dissipate power (heaters, motors, etc.) have positive power
Things which supply power (batteries, generators) have negative power

## Slide 27: Power
Power is important for two reasons
  Conservation of energy
    DC/DC converters are used to convert electricity at one voltage to another voltage
    If you have 1 A at 12 V (12 W) going into a 12->5 DC/DC converter, you can get no more than 2.4 A at 5 V (12 W) out of it
  Most components have power limits
    A 10 Ω resistor rated at 0.25 W could handle ~160 mA
    If you try to run an amp through it, it will burn up
    In most cases, this is a thermal constraint; dissipating more heat requires a higher temperature, and components have maximum temperatures

## Slide 28: I-V Plots
Plots of current vs. voltage
Current is considered positive if it flows from the positive pole of a component to the negative pole
In this circuit, the battery is seeing negative current, and the resistor is seeing positive current
+
-

## Slide 29: I-V Plots
Chart: Voltage (V)

## Slide 30: I-V Plots
Chart: Voltage (V)
| -5 | -4.9000000000000004 | -4.8 | -4.7 | -4.5999999999999996 | -4.5 | -4.4000000000000004 | -4.3 | -4.2 | -4.0999999999999996 | -4 | -3.9 | -3.8 | -3.7 | -3.6 | -3.5000000000000102 | -3.4000000000000101 | -3.30000000000001 | -3.2000000000000099 | -3.1000000000000099 | -3.0000000000000102 | -2.9000000000000101 | -2.80000000000001 | -2.7000000000000099 | -2.6000000000000099 | -2.5000000000000102 | -2.4000000000000101 | -2.30000000000001 | -2.2000000000000099 | -2.1000000000000099 | -2.0000000000000102 | -1.9000000000000099 | -1.80000000000001 | -1.7000000000000099 | -1.6000000000000101 | -1.50000000000001 | -1.4000000000000099 | -1.30000000000001 | -1.2000000000000099 | -1.1000000000000101 | -1.00000000000001 | -0.90000000000001001 | -0.80000000000001004 | -0.70000000000002005 | -0.60000000000001996 | -0.50000000000001998 | -0.40000000000002001 | -0.30000000000001997 | -0.20000000000002 | -0.10000000000002 | -2.0428103653102899E-14 | 9.9999999999980105E-2 | 0.19999999999998 | 0.29999999999998 | 0.39999999999997998 | 0.49999999999998002 | 0.59999999999997999 | 0.69999999999997997 | 0.79999999999997995 | 0.89999999999998004 | 0.99999999999998002 | 1.0999999999999801 | 1.19999999999998 | 1.2999999999999801 | 1.3999999999999799 | 1.49999999999998 | 1.5999999999999801 | 1.69999999999998 | 1.7999999999999801 | 1.8999999999999799 | 1.99999999999998 | 2.0999999999999699 | 2.19999999999997 | 2.2999999999999701 | 2.3999999999999702 | 2.4999999999999698 | 2.5999999999999699 | 2.69999999999997 | 2.7999999999999701 | 2.8999999999999702 | 2.9999999999999698 | 3.0999999999999699 | 3.19999999999997 | 3.2999999999999701 | 3.3999999999999702 | 3.4999999999999698 | 3.5999999999999699 | 3.69999999999997 | 3.7999999999999701 | 3.8999999999999702 | 3.9999999999999698 | 4.0999999999999703 | 4.19999999999997 | 4.2999999999999696 | 4.3999999999999702 | 4.4999999999999698 | 4.5999999999999703 | 4.69999999999997 | 4.7999999999999696 | 4.8999999999999604 | 4.99999999999996
1W Power | -0.2 | -0.20408 | -0.20833 | -0.21277 | -0.21739 | -0.22222 | -0.22727 | -0.23256 | -0.2381 | -0.2439 | -0.25 | -0.25641 | -0.26316 | -0.27027 | -0.27778 | -0.28571 | -0.29412 | -0.30303 | -0.3125 | -0.32258 | -0.33333 | -0.34483 | -0.35714 | -0.37037 | -0.38462 | -0.4 | -0.41667 | -0.43478 | -0.45455 | -0.47619 | -0.5 | -0.52632 | -0.55556 | -0.58824 | -0.625 | -0.66667 | -0.71429 | -0.76923 | -0.83333 | -0.90909 | -1 | -1.1111 | -1.25 | -1.4286 | -1.6667 | -2 | -2.5 | -3.3333 | -5 | -10
-1W Power | 0.2 | 0.20408 | 0.20833 | 0.21277 | 0.21739 | 0.22222 | 0.22727 | 0.23256 | 0.2381 | 0.2439 | 0.25 | 0.25641 | 0.26316 | 0.27027 | 0.27778 | 0.28571 | 0.29412 | 0.30303 | 0.3125 | 0.32258 | 0.33333 | 0.34483 | 0.35714 | 0.37037 | 0.38462 | 0.4 | 0.41667 | 0.43478 | 0.45455 | 0.47619 | 0.5 | 0.52632 | 0.55556 | 0.58824 | 0.625 | 0.66667 | 0.71429 | 0.76923 | 0.83333 | 0.90909 | 1 | 1.1111 | 1.25 | 1.4286 | 1.6667 | 2 | 2.5 | 3.3333 | 5 | 10
2W Power | -0.4 | -0.40816 | -0.41667 | -0.42553 | -0.43478 | -0.44444 | -0.45455 | -0.46512 | -0.47619 | -0.4878 | -0.5 | -0.51282 | -0.52632 | -0.54054 | -0.55556 | -0.57143 | -0.58824 | -0.60606 | -0.625 | -0.64516 | -0.66667 | -0.68966 | -0.71429 | -0.74074 | -0.76923 | -0.8 | -0.83333 | -0.86957 | -0.90909 | -0.95238 | -1 | -1.0526 | -1.1111 | -1.1765 | -1.25 | -1.3333 | -1.4286 | -1.5385 | -1.6667 | -1.8182 | -2 | -2.2222 | -2.5 | -2.8571 | -3.3333 | -4 | -5 | -6.6667 | -10 | -20
-2W Power | 0.4 | 0.40816 | 0.41667 | 0.42553 | 0.43478 | 0.44444 | 0.45455 | 0.46512 | 0.47619 | 0.4878 | 0.5 | 0.51282 | 0.52632 | 0.54054 | 0.55556 | 0.57143 | 0.58824 | 0.60606 | 0.625 | 0.64516 | 0.66667 | 0.68966 | 0.71429 | 0.74074 | 0.76923 | 0.8 | 0.83333 | 0.86957 | 0.90909 | 0.95238 | 1 | 1.0526 | 1.1111 | 1.1765 | 1.25 | 1.3333 | 1.4286 | 1.5385 | 1.6667 | 1.8182 | 2 | 2.2222 | 2.5 | 2.8571 | 3.3333 | 4 | 5 | 6.6667 | 10 | 20
4W Power | -0.8 | -0.81633 | -0.83333 | -0.85106 | -0.86957 | -0.88889 | -0.90909 | -0.93023 | -0.95238 | -0.97561 | -1 | -1.0256 | -1.0526 | -1.0811 | -1.1111 | -1.1429 | -1.1765 | -1.2121 | -1.25 | -1.2903 | -1.3333 | -1.3793 | -1.4286 | -1.4815 | -1.5385 | -1.6 | -1.6667 | -1.7391 | -1.8182 | -1.9048 | -2 | -2.1053 | -2.2222 | -2.3529 | -2.5 | -2.6667 | -2.8571 | -3.0769 | -3.3333 | -3.6364 | -4 | -4.4444 | -5 | -5.7143 | -6.6667 | -8 | -10 | -13.3333 | -20 | -40
-4W Power | 0.8 | 0.81633 | 0.83333 | 0.85106 | 0.86957 | 0.88889 | 0.90909 | 0.93023 | 0.95238 | 0.97561 | 1 | 1.0256 | 1.0526 | 1.0811 | 1.1111 | 1.1429 | 1.1765 | 1.2121 | 1.25 | 1.2903 | 1.3333 | 1.3793 | 1.4286 | 1.4815 | 1.5385 | 1.6 | 1.6667 | 1.7391 | 1.8182 | 1.9048 | 2 | 2.1053 | 2.2222 | 2.3529 | 2.5 | 2.6667 | 2.8571 | 3.0769 | 3.3333 | 3.6364 | 4 | 4.4444 | 5 | 5.7143 | 6.6667 | 8 | 10 | 13.3333 | 20 | 40
8W Power | -1.6 | -1.6327 | -1.6667 | -1.7021 | -1.7391 | -1.7778 | -1.8182 | -1.8605 | -1.9048 | -1.9512 | -2 | -2.0513 | -2.1053 | -2.1622 | -2.2222 | -2.2857 | -2.3529 | -2.4242 | -2.5 | -2.5806 | -2.6667 | -2.7586 | -2.8571 | -2.963 | -3.0769 | -3.2 | -3.3333 | -3.4783 | -3.6364 | -3.8095 | -4 | -4.2105 | -4.4444 | -4.7059 | -5 | -5.3333 | -5.7143 | -6.1538 | -6.6667 | -7.2727 | -8 | -8.8889 | -10 | -11.4286 | -13.3333 | -16 | -20 | -26.6667 | -40 | -80
-8W Power | 1.6 | 1.6327 | 1.6667 | 1.7021 | 1.7391 | 1.7778 | 1.8182 | 1.8605 | 1.9048 | 1.9512 | 2 | 2.0513 | 2.1053 | 2.1622 | 2.2222 | 2.2857 | 2.3529 | 2.4242 | 2.5 | 2.5806 | 2.6667 | 2.7586 | 2.8571 | 2.963 | 3.0769 | 3.2 | 3.3333 | 3.4783 | 3.6364 | 3.8095 | 4 | 4.2105 | 4.4444 | 4.7059 | 5 | 5.3333 | 5.7143 | 6.1538 | 6.6667 | 7.2727 | 8 | 8.8889 | 10 | 11.4286 | 13.3333 | 16 | 20 | 26.6667 | 40 | 80
 | 10 | 5 | 3.3333 | 2.5 | 2 | 1.6667 | 1.4286 | 1.25 | 1.1111 | 1 | 0.90909 | 0.83333 | 0.76923 | 0.71429 | 0.66667 | 0.625 | 0.58824 | 0.55556 | 0.52632 | 0.5 | 0.47619 | 0.45455 | 0.43478 | 0.41667 | 0.4 | 0.38462 | 0.37037 | 0.35714 | 0.34483 | 0.33333 | 0.32258 | 0.3125 | 0.30303 | 0.29412 | 0.28571 | 0.27778 | 0.27027 | 0.26316 | 0.25641 | 0.25 | 0.2439 | 0.2381 | 0.23256 | 0.22727 | 0.22222 | 0.21739 | 0.21277 | 0.20833 | 0.20408 | 0.2
 | -10 | -5 | -3.3333 | -2.5 | -2 | -1.6667 | -1.4286 | -1.25 | -1.1111 | -1 | -0.90909 | -0.83333 | -0.76923 | -0.71429 | -0.66667 | -0.625 | -0.58824 | -0.55556 | -0.52632 | -0.5 | -0.47619 | -0.45455 | -0.43478 | -0.41667 | -0.4 | -0.38462 | -0.37037 | -0.35714 | -0.34483 | -0.33333 | -0.32258 | -0.3125 | -0.30303 | -0.29412 | -0.28571 | -0.27778 | -0.27027 | -0.26316 | -0.25641 | -0.25 | -0.2439 | -0.2381 | -0.23256 | -0.22727 | -0.22222 | -0.21739 | -0.21277 | -0.20833 | -0.20408 | -0.2
 | 20 | 10 | 6.6667 | 5 | 4 | 3.3333 | 2.8571 | 2.5 | 2.2222 | 2 | 1.8182 | 1.6667 | 1.5385 | 1.4286 | 1.3333 | 1.25 | 1.1765 | 1.1111 | 1.0526 | 1 | 0.95238 | 0.90909 | 0.86957 | 0.83333 | 0.8 | 0.76923 | 0.74074 | 0.71429 | 0.68966 | 0.66667 | 0.64516 | 0.625 | 0.60606 | 0.58824 | 0.57143 | 0.55556 | 0.54054 | 0.52632 | 0.51282 | 0.5 | 0.4878 | 0.47619 | 0.46512 | 0.45455 | 0.44444 | 0.43478 | 0.42553 | 0.41667 | 0.40816 | 0.4
 | -20 | -10 | -6.6667 | -5 | -4 | -3.3333 | -2.8571 | -2.5 | -2.2222 | -2 | -1.8182 | -1.6667 | -1.5385 | -1.4286 | -1.3333 | -1.25 | -1.1765 | -1.1111 | -1.0526 | -1 | -0.95238 | -0.90909 | -0.86957 | -0.83333 | -0.8 | -0.76923 | -0.74074 | -0.71429 | -0.68966 | -0.66667 | -0.64516 | -0.625 | -0.60606 | -0.58824 | -0.57143 | -0.55556 | -0.54054 | -0.52632 | -0.51282 | -0.5 | -0.4878 | -0.47619 | -0.46512 | -0.45455 | -0.44444 | -0.43478 | -0.42553 | -0.41667 | -0.40816 | -0.4
Remember: P=IV

## Slide 31: LED
Typical I-V plot for a high-power LED
Chart: 

## Slide 32: LED
Generally, we want to squeeze as much light as we can out of an LED, without burning it up
Therefore, we want to keep the operating point close to the current limit, but not over it
To achieve this, we can:
  Use a power supply that tries to maintain a specified voltage (voltage source)
  Use a power supply that tries to maintain a specified current (current source)

## Slide 33: LED
Chart: 
Min Voltage | -5 | 5
Max Voltage | -5 | 5
To stay in this section of the curve, we can either:
  Maintain voltage between 3.177 V and 3.200 V, OR
  Maintain current between 0.944 A and 1.000 A
Voltage control requires PS accuracy of 0.7%
Current control requires PS accuracy of 5.6%
This is why constant-current power supplies are usually used to drive large LEDs
  Current control requires less accuracy than voltage control