## Slide 1: Line-Replaceable Units
Modularity, Integration, Encapsulation, and Interface Control

## Slide 2: Overview
What is modularity?
  Mechanical
    Specify envelopes, mass
  Electrical
    Specify interfaces
  Programming
  Logistical
    Parallelism
    Servicability
What is integration?
What is encapsulation?
ICD

## Slide 3: Integration
What is integration?
  To me, integration means lots of complex interdependencies
  A given component can serve several different purposes, and there are many interactions between components
This is not necessarily a bad thing
  It may lead to a more optimized final design
    For example: a robot needs chassis rails, as a place to mount the wheels to
    A robot also needs a bellypan, as a place to mount electronics
    If the bellypan geometry and mounting is correct, it can lend significant strength to the chassis, allowing you to use thinner tube

## Slide 4: Integration
However, highly integrated designs tend to require a lot more design effort, have more complex failure modes, and require special handing and maintenance
Consider the Atlas ICBM
The Atlas has “balloon tanks”
  The fuel tanks are very thin and flexible, like balloons
  Unlike most other rockets, the tanks must always be pressurized, otherwise they collapse
  Tanks fulfil both a fuel storage function and a structural function
Balloon tanks allow much lighter construction
However, the pressurization issue makes them so problematic that they’re not used anymore

## Slide 5: Integration
Our robots tend to be very highly integrated
Many control system components built into the superstructure
Electronics bolted to bellypan, then wired together
Many structural components also serve as wire management
Try swapping the PDP on the 2019 bot…

## Slide 6: Process Flow

## Slide 7: Problems With “Waterfall” Process
Allows a high level of integration, because the entire robot is being designed in one process
Introduces dependencies between processes
  Can’t make sure WiFi works until robot is wired, which can’t happen until robot is assembled
Boom-and-bust workload for subteams
  The control system team can’t start programming the robot until the robot is mostly done
  Applies to manufacturing, to a more limited extent

## Slide 8: Modularity
What is modularity?
Composition becomes more hierarchical
Instead of a robot made of components, the robot is made of subsystems
Subsystems are independently designed, built, and tested before being assembled into “the robot”

## Slide 9: Modularity
Instead of the robot being highly integrated, the subsystems are highly integrated
Subsystems should be well encapsulated (software engineering term)
“Things outside the boundary don’t affect things inside the boundary”
Things outside the boundary only need to care about the interface

## Slide 10: Example
We (JPL) are building a spacecraft, and we want to put a camera on it
We contract out the design & manufacture of the camera
But how do we make sure the camera will work correctly with the rest of the spacecraft?
We agree on the interfaces, in the form of an ICD (Interface Control Document)

## Slide 11: Example
Mechanical ICD (MICD)
  Mass
  Center of mass
  Envelopes

## Slide 12: Example
Electrical ICD (EICD)
  Power requirements
  Connectors & pinouts
  Data transfer (Ethernet, serial, etc.)

## Slide 13: Example
Communications (programming)
  Command dictionary
  Data encoding
  State diagrams

## Slide 14: Example

## Slide 15: Results
Thanks to a bilateral ICD, the contractor was designing, building, and testing the camera while we were designing, building, and testing the spacecraft
When the contractor delivers the camera:
  We bolt it onto the mount we’d already made
  We plug in the connectors we’d already wired
  We run the software we’d already written
  Since the spacecraft complies with the ICD, and the camera complies with the ICD, they should work together after being tested independently

## Slide 16: Modularity & Integration
Modularity and integration are not contradictory
Modularity just requires that your “tight” integration be at the subsystem level, rather than the system level
Subsystems might be complex and tightly-integrated, but their interfaces are well-defined

## Slide 20: New Process Flow

## Slide 21: JSOW
Joint StandOff Weapon
“…JSOW was considered to be one of the most successful development programs in DOD history...”
“…introduced to operational use a year ahead of schedule.”
“…never had a weight management problem, and was deployed at its target weight.”
“…was able to obtain authority from an independent safety review in record time.”
Quotes from Wikipedia

## Slide 22: JSOW
“The program staff was organized into integrated product teams with members from the government, the prime Texas Instruments and subcontractors.”